Research Proposal for Bachelor Thesis Project

Student name:	Jakob Lüdke
Student number:	21-948-559
Student email:	luedkej@ethz.ch
Advisors:	Alexander Oing
Prof. Dr. Christoph R. Müller
Topic: Development of a tandem catalyst system for the single pass conversion of CO2 to higher alcohols optimized in Propylen selectivity

Why is this topic important?
In light of the ever-increasing concentration of CO2 in the atmosphere and the resulting intensification of the greenhouse effect, it is desirable not only to reduce future CO2 emissions but also to develop methods for utilizing the CO2 already present in the air. [1]
One particularly promising approach to recycle CO2 chemically is its hydrogenation into higher alcohols, which serve as platform chemicals to produce e.g. polymers and perfumes.
Due to the reaction kinetics, the educts´ thermodynamic properties (e.g. CO2 and H2) and the intermediates formed during the reaction like methanol, catalytic control is necessary to achieve the highest possible yield of higher alcohols. [2] Alcohol production occurs in two steps: first, CO2 is hydrogenated with H2 to form light olefins, followed by the hydroformylation of these olefins into alcohols.
By selecting the appropriate catalysts, the formation of specific olefins such as ethylene or propylene can be promoted. The goal is to optimize the production of the olefin that yields the highest amount of alcohol during the hydroformylation process. Therefore, the catalyst of choice should promote the formulation of the olefin that the hydroformylation catalyst has the highest selectivity to.
What has been done so far? What was observed? What are the research gaps?
In previously published studies on the development of a tandem catalyst system for the conversion of CO2 into higher alcohols, a RhCo3/MCM-41 catalyst was used for the hydroformylation reaction. Based on the assumption that this catalyst exhibits increased selectivity for ethylene, the catalyst used for hydrogenation was optimized to maximize ethylene output. A ZnZrOx/SAPO-34 solid soultion, with a Si/Al ratio of 0.30, was found to be the most effective catalyst for ethylene production. [3]
However, contrary to expectations, a higher yield of 1-butanol than 1-propanol was observed, suggesting increased selectivity for propylene by the Rh catalyst, instead of the expected ethylene selectivity.
In light of this, a catalyst that optimizes propylene output during the hydrogenation reaction promises a higher alcohol yield. Recent studies indicate that a ZnZrOx/SSZ-13 catalyst is significantly more suitable than the previously used ZnZrOx/SAPO-34 solid solution for maximizing propylene output, due to its concentrated tetramethylbenzene. The Si/Al ratio is highlighted as a key optimization parameter for both solutions. [4]
3. What will be done? What research gap am I filling?
As part of this project, an existing tandem catalyst system will be modified to maximize the output of propylene instead of ethylene during the hydrogenation of CO2. [3]
To achieve this, the current ZnZrOx/SAPO-34 catalyst will be replaced with a ZnZrOx/SSZ-13 solid solution.
The first step will be to determine the Si/Al ratio that maximizes the propylene yield for the new catalyst. Subsequently, the system parameters—such as pressure and flow rate—will be adjusted to match the new reaction kinetics of the tandem system in order to maximize the yield of higher alcohols.

This thesis proposal…
…has been created by	…is agreed on by
Student:	Supervisor:
____________________________	____________________________
Date, Signature	Date, Signature

References

[1]	NOAA Global Monitoring Laboratory - Trends in Atmospheric Carbon Dioxide (2024); EPA based	on various sources (2022) – with major processing by Our World in Data

[2]	F. Zeng, C. Mebrahtu, X. Xi, L. Liao, J. Ren, J. Xie, H. J. Heeres, and R. Palkovits. “Catalysts design	for higher alcohols synthesis by CO2 hydrogenation: Trends and future perspectives”. In: Applied	Catalysis B: Environmental 291 (Aug. 2021), page 120073. issn: 09263373. doi:	10.1016/j.apcatb.2021.120073. url: https://linkinghub.elsevier.com/retrieve/pii/S0926337321001995.

[3]	F. Arnet, “Development and study of a tandem catalyst system for the single-pass conversion of CO2	to higher alcohols”, 2024

[4]	S. Chen, J. Wang, Z. Feng, Y. Jiang, H. Hu, Y. Qu, S. Tang, Z. Li, J. Liu, J. Wang, C. Li, Angew.	Chem. Int. Ed. 2024, 63, e202316874. https://doi.org/10.1002/anie.202316874